## Slide 1
Second Week
17 Apr 23 -21 Apr 23
Presentation
SPORT LAB
Present by: Suhas Somashekar
Instructor：Prof. Pedram
Mentor: Arash Fayyazi

## Slide 2
CONTENTS
A Review of our existing code
Suggestions for improving the optimization
Winograd Fast Convolution
Pruning And Quantization
Dynamic Tiling
Cache Aware Tiling
Dynamic scheduling and adaptive mapping
Heuristic-based search
Model Approximation
Overview of Interstellar
DNN Accelerator Design Space
Other important details from the paper
Overview of the Code of Interstellar-CNN-scheduler
Loop Blocking and Resource Allocation
Spatial Loop Unrolling

## Slide 3
The current code uses tiling optimization for a convolutional layer in a neural network. It aims to find the best tiling and order for a given set of convolution parameters to minimize the computation cycles and energy consumption.
The code leverages the following methods for optimization:
  Loop Permutations: It generates permutations for the order of the loops in the optimization process. The order of loops can have a significant impact on the performance and energy consumption.
  Input, Output, and Weight Stationary Energy Calculation: The code calculates energy consumption for input stationary, output stationary, and weight stationary schemes and selects the one with the lowest energy consumption.
  Parallel and Sequential Processing: The code supports both parallel and sequential processing, where parallel processing utilizes multiple cores for faster optimization.
A Review of our existing code – “optimize_for_order”

## Slide 4
To further improve the optimization, we can consider the following suggestions:
Winograd Convolution Algorithm: The Winograd algorithm can significantly reduce the number of multiplications required for convolution, improving performance and energy efficiency. Incorporate the Winograd algorithm into the optimization process.
Pruning and Quantization: Apply pruning to remove insignificant weights and quantization to reduce the precision of weights and activations. These techniques can reduce memory requirements and computation complexity while maintaining model accuracy.
Dynamic Tiling: Instead of using static tiling, use dynamic tiling based on the input data and layer characteristics. This can lead to more efficient memory access patterns and reduced energy consumption.
Cache-aware Tiling: Modify the optimization process to be cache-aware, considering the memory hierarchy (cache sizes and associativity) of the underlying hardware. This can help in reducing cache misses and improve overall performance.
Dynamic scheduling and adaptive mapping: Implement a dynamic scheduling approach that adapts to varying workloads and hardware conditions. This could involve monitoring the workload and hardware state at runtime and adjusting the mapping accordingly to optimize performance and energy efficiency.
Heuristic-based search: By employing heuristic-based search techniques, we can find near-optimal solutions for mapping CNNs onto hardware accelerators more efficiently than exhaustive search methods, leading to improved performance and energy efficiency.
Model Approximation: This reduces the number of parameters and computations, leading to a more efficient execution on hardware accelerators.
Suggestions for improving the optimization

## Slide 5
Winograd Fast Convolution
Winograd Fast Convolution is an algorithm that accelerates the computation of convolutional layers in Convolutional Neural Networks (CNNs). The method, developed by Shmuel Winograd, is based on the Winograd minimal filtering algorithm, which reduces the number of multiplications required in the convolution process.
In a standard convolution operation, each output element is computed as the sum of products between input and kernel (filter) elements. For an input matrix of size NxN and a filter of size FxF, this involves N²F² multiplications and N²(F²-1) additions. As the size of the input and filters increases, the number of operations grows significantly, making the convolution computationally expensive.
Winograd Fast Convolution focuses on reducing the number of multiplications, as they are typically more time-consuming than additions. The idea is to transform the input and filter matrices into a different domain where element-wise products can be computed more efficiently. The output is then transformed back into the original domain to obtain the final result.
The algorithm uses small tiles of the input and filter matrices and takes advantage of the properties of polynomial multiplication. In the case of 3x3 filters, the most common case in practice, the Winograd algorithm reduces the number of multiplications per output element from 9 to 4, which is a significant speedup.
In summary, Winograd Fast Convolution is an efficient algorithm for computing convolutions in neural networks, especially for large input and filter sizes. It reduces the computational complexity by minimizing the number of multiplications required and has been adopted in various deep learning frameworks to accelerate training and inference.
References:
https://arxiv.org/pdf/2209.12982.pdf
https://arxiv.org/abs/2201.10369

## Slide 6
Pruning And Quantization
To add pruning and quantization to the existing code, we can follow these steps:
Implement pruning by removing low-weight connections. For this, we can use a threshold value to remove connections with weights below the threshold.
Implement quantization by reducing the precision of weights and activations in the network.
Sample steps:
Choose a baseline precision: Start with a common precision, such as 32-bit floating-point (FP32) or 16-bit floating-point (FP16) for both input and weight data. This will be a baseline for comparing the performance and accuracy of our model with different precision settings.
Quantization: Quantization is the process of converting a higher precision model (e.g., FP32 or FP16) to a lower precision model, such as fixed-point representation (e.g., INT8, INT16).
Fine-tuning: After quantization, the model may experience a drop in accuracy. To mitigate this, fine-tune the quantized model by retraining it with a lower learning rate for a few epochs on the training dataset. This process helps the model adapt to the reduced precision and regain some of the lost accuracy.
Evaluate performance and accuracy: Evaluate the quantized model's performance and accuracy on the validation dataset. Compare these metrics with the baseline model to assess the impact of reduced precision on our specific model and dataset.
Iteratively adjust precision: If the quantized model's performance and accuracy are not satisfactory, iteratively adjust the input and weight precision values. Experiment with different combinations of input and weight precisions, and repeat steps 2 to 4 to find the optimal balance between performance, resource utilization, and accuracy.
References: https://arxiv.org/pdf/2101.09671.pdf
https://www.ncbi.nlm.nih.gov/pmc/articles/PMC8122998/

## Slide 7
for _iprec in range(min_iprec, max_iprec + 1):
  for _wprec in range(min_wprec, max_wprec + 1):
    new_conv_params = (
    acc_obj, K, O, S, IC, OC, B, _iprec, _wprec, im2col, energy_cost, pool_kernel, pool_stride
    )
    for _b in range(num_B_tiles):
      for _oc in range(num_OC_tiles):
        if best_cycles is None or best_cycles > cycles or (best_cycles == cycles and best_energy > energy):
        best_energy = energy
        best_cycles = cycles
        best_mem_cycles = mem_cycles
        best_order = order_type
        best_tiling = tiling
        best_iprec = _iprec
        best_wprec = _wprec
return (best_tiling, order_type, best_cycles, best_energy, best_iprec, best_wprec, cycle_array, energy_array)

## Slide 8
# ... (existing code)
# Add these functions
def prune_weights(weights, threshold):
  pruned_weights = copy.deepcopy(weights)
  pruned_weights[np.abs(pruned_weights) < threshold] = 0
  return pruned_weights
def quantize_weights(weights, bitwidth):
  kmeans = KMeans(n_clusters=2 ** bitwidth)
  kmeans.fit(weights.reshape(-1, 1))
  quantized_weights = kmeans.cluster_centers_[kmeans.labels_].reshape(weights.shape)
  return quantized_weights
# Update the optimize_for_order function
def optimize_for_order(conv_params, pool_kernel=None, pool_stride=None, sequential=True, pruning_threshold=None, quantization_bitwidth=None):
# ... (existing code)
  if pruning_threshold is not None:
  weights = np.random.randn(OC, IC, K, K) # Replace with actual weights
  pruned_weights = prune_weights(weights, pruning_threshold)
  # Replace original weights with pruned_weights in the model
  if quantization_bitwidth is not None:
  weights = np.random.randn(OC, IC, K, K) # Replace with actual weights
  quantized_weights = quantize_weights(weights, quantization_bitwidth)
  # Replace original weights with quantized_weights in the model
# ... (existing code)

## Slide 9
Dynamic Tiling
(Wanted Confirmation if we are adopting static tiling or dynamic tiling in our current architecture)
Analyzing the DNN architecture: The compiler examines the DNN architecture to understand the dimensions and data dependencies of each layer, which helps determine suitable tiling configurations.
Selecting tile sizes: The compiler chooses appropriate tile sizes based on the available FPGA resources, layer dimensions, and performance requirements. The tile sizes may vary for different layers or even within a single layer.
Mapping tiles to FPGA resources: The compiler maps the tiled computation onto the FPGA's hardware resources, considering the available computing units, memory hierarchy, and I/O bandwidth. This can involve techniques such as loop unrolling, pipelining, or parallelization to maximize throughput and minimize latency.
Scheduling and execution: The compiler schedules the execution of the tiled computation on the FPGA, ensuring that the required data and resources are available when needed. This can involve dynamic scheduling techniques that adapt to varying resource utilization or data availability.

## Slide 10
Cache Aware Tiling
Cache-aware tiling aims to minimize cache misses, reduce data movement between different memory levels, and maximize cache utilization to boost the performance of the DNN.
Analyzing the DNN architecture and memory hierarchy: The compiler examines the DNN architecture, layer dimensions, and data dependencies, as well as the FPGA's memory hierarchy, including cache sizes and access latencies.
Selecting tile sizes based on cache constraints: The compiler chooses appropriate tile sizes that take into account the available cache sizes, ensuring that each tile fits within the cache to minimize cache misses and data movement. The tile sizes may vary for different layers or even within a single layer, depending on the cache constraints and layer dimensions.
Mapping tiles to FPGA resources: The compiler maps the tiled computation onto the FPGA's hardware resources, considering cache constraints and aiming to maximize cache utilization. This can involve techniques such as loop unrolling, pipelining, or parallelization to maximize throughput and minimize latency.
Scheduling and execution: The compiler schedules the execution of the tiled computation on the FPGA, ensuring that the required data and resources are available when needed and that cache reuse is maximized. This can involve dynamic scheduling techniques that adapt to varying resource utilization or data availability.
References: https://capra.cs.cornell.edu/latte23/paper/7.pdf

## Slide 11
Dynamic scheduling and adaptive mapping
Dynamic scheduling and adaptive mapping refer to strategies that adjust the mapping of CNNs onto hardware accelerators at runtime, based on changing workloads, hardware conditions, or other factors. These techniques can help optimize the performance, energy efficiency, and resource utilization of hardware accelerators, especially when dealing with diverse and dynamic application scenarios.
Steps:
Monitoring: The first step in implementing dynamic scheduling and adaptive mapping is to monitor the workload and hardware state. This could involve collecting metrics such as layer dimensions, input data size, memory usage, computation load, temperature, power consumption, or other relevant factors.
Decision-making: Based on the monitored data, the scheduler can make decisions to adjust the mapping. For example, it could re-order loops, change blocking sizes, or modify dataflow patterns to better match the current workload and hardware conditions. The decision-making process could employ machine learning techniques, heuristics, or other optimization algorithms to determine the best course of action.
Adaptation: Once the scheduler has made a decision, it needs to apply the changes to the hardware accelerator. This could involve reconfiguring the hardware resources, adjusting the control signals, or modifying the data layout in memory. The adaptation should be performed with minimal overhead to ensure that the benefits of the new mapping outweigh the costs of the adaptation process.
Continuous optimization: Dynamic scheduling and adaptive mapping are not one-time processes. The scheduler should continuously monitor the workload and hardware state, making decisions and adapting the mapping as needed to maintain optimal performance and energy efficiency.
Some potential benefits of dynamic scheduling and adaptive mapping are:
Improved performance: By adapting the mapping to match the current workload and hardware conditions, dynamic scheduling and adaptive mapping can help maximize the utilization of hardware resources, resulting in better overall performance.
Energy efficiency: Adapting the mapping can also help minimize power consumption by optimizing data movement and computation patterns.
Robustness: Dynamic scheduling and adaptive mapping can make the scheduler more robust to variations in workloads, hardware conditions, or other factors that could impact performance and energy efficiency.
References: https://cseweb.ucsd.edu/~hadi/doc/paper/2019-icml-release.pdf
https://dl.acm.org/doi/10.1145/3533251

## Slide 12
Heuristic-based search
Instead of exhaustively searching all possible tiling configurations, we can employ heuristics to guide the search, such as genetic algorithms, simulated annealing, or other optimization techniques. These methods can help us find good tiling configurations more efficiently by searching a smaller subset of the solution space.
Here are some examples of heuristic-based search techniques that can be employed for this purpose:
Genetic algorithms: Genetic algorithms are inspired by the process of natural selection and genetic inheritance. They maintain a population of candidate solutions and evolve it over time through operations like selection, crossover, and mutation. This approach can be applied to optimize loop orderings or blocking sizes by representing each candidate solution as a chromosome and evolving the population towards better solutions.
Simulated Annealing: Simulated Annealing is a probabilistic optimization technique that mimics the annealing process in metallurgy. It starts with an initial solution and iteratively perturbs it to explore the search space. The acceptance probability of a new solution depends on the difference in cost and a temperature parameter that gradually decreases over time. This approach helps avoid getting stuck in local minima and can be applied to optimize various aspects such as loop orderings or dataflow patterns.
Particle Swarm Optimization (PSO): PSO is a population-based optimization technique inspired by the social behavior of bird flocks or fish schools. Each particle in the swarm represents a candidate solution and moves through the search space guided by its personal best solution and the global best solution found so far. This approach can be used for optimizing blocking sizes, loop orderings, and resource allocation.
Hill Climbing: Hill Climbing is an iterative optimization algorithm that starts with an initial solution and explores the neighboring solutions by making small modifications. If a neighboring solution is better, it becomes the new current solution. This process is repeated until no better neighboring solution is found. Hill Climbing can be applied to optimize loop orderings, blocking sizes, and dataflow patterns.
When incorporating heuristic-based search methods, it is essential to:
Select an appropriate heuristic-based search algorithm based on the problem characteristics and the target hardware platform.
Define a suitable cost function that captures the objectives of the optimization, such as minimizing energy consumption, latency, or resource utilization.
Adapt the algorithm to handle problem-specific constraints, such as hardware limitations, memory capacity, or parallelism requirements.
References: https://cseweb.ucsd.edu/~hadi/doc/paper/2019-icml-release.pdf

## Slide 13
Model Approximation
References: https://workshops.inf.ed.ac.uk/accml/papers/2021/3rd_AccML_paper_2.pdf

## Slide 14: Overview of Interstellar
Interstellar: Using Halide’s Scheduling Language to Analyze DNN Accelerators

## Slide 15
Algorithm 1 describes the computation process for a convolutional (CONV) layer in a deep neural network (DNN). This process involves seven nested loops iterating over different dimensions of the input and output tensors, as well as the convolutional kernel (filter) weights.
Here's a breakdown of each loop variable:
b: batch index, iterating from 0 to B-1, where B is the batch size. This loop iterates over each sample in the batch.
k: output channel index, iterating from 0 to K-1, where K is the number of output channels (feature maps) in the layer.
c: input channel index, iterating from 0 to C-1, where C is the number of input channels.
y: output height index, iterating from 0 to Y-1, where Y is the height of the output feature map.
x: output width index, iterating from 0 to X-1, where X is the width of the output feature map.
fy: filter height index, iterating from 0 to FY-1, where FY is the height of the filter kernel.
fx: filter width index, iterating from 0 to FX-1, where FX is the width of the filter kernel.
During each iteration of the innermost loop, the algorithm performs the following computation:
O[b][k][x][y] += I[b][c][x+fx][y+fy] * W[k][c][fx][fy]
This line computes a dot product between the input tensor I and the filter weights W, taking into account the input and output channels, as well as the spatial dimensions of the input and output feature maps. The result is added to the corresponding position in the output tensor O.
By iterating through all possible combinations of input and output channels, input and output spatial positions, and filter kernel positions, the algorithm computes the complete output tensor for the CONV layer. The nested loops ensure that every element of the output feature maps is populated with the result of the convolution operation between the input feature maps and the filter kernels.
Standard Convolution Algorithm

## Slide 16: DNN Accelerator Design Space
The DNN accelerator design space, consists of three dimensions:
Dataflow: This dimension considers how the computation is scheduled across multiple processing elements (PEs) and how data is accessed and communicated between them. It aims to minimize data access to more expensive memory types and maximize data reuse.
Resource Allocation: This dimension involves allocating hardware resources such as the dimensions of the PE array and the size of each level in the memory hierarchy. It aims to balance throughput, data locality, and energy cost.
Loop Blocking: This dimension focuses on scheduling computation to maximize data reuse in smaller, nearer memories, which can lower overall energy cost. It includes techniques like loop blocking and reordering.
Considering these three factors allows for a comprehensive and systematic design space.

## Slide 17
-The data communication pattern is determined by which loops are spatially unrolled in hardware and which are not.
-Spatial loop unrolling in hardware refers to mapping particular loops to parallel computation structures.
-Syntax U | V, where U and V represent loops unrolled across the vertical and horizontal dimensions, respectively.
-Replication processes multiple small loops in parallel to increase resource utilization
-the loop-based taxonomy can express this improvement using U | VW or UW | V.
-When replication is supported, the data communication pattern becomes non-uniform(intra-loop data can be communicated among nearest-neighbor PEs, while inter-loop data have to be sent multiple hops away with higher communication cost.)
- the ordering of loops mapped to the same dimension to represent different communication distances. The loop-based approach builds upon stationary characteristics and offers a more precise definition of each dataflow while expanding the range of flows that can be described.
-The loop-based dataflow taxonomy allows dataflows and loop blocking schemes to be expressed as transformations of the nested loops in Algorithm 1. This enables using existing approaches to find loop transformations that optimize cost functions for software implementations or hardware designs.
Other important details from the paper

## Slide 18
Here is an overview of the structure of Interstellar-CNN-scheduler ()
1. `main.py`: The entry point of the tool, where the main function resides. It initializes the necessary resources and layers, and then calls the dataflow exploration function from `mapping_point_generator.py`.
2. `mapping_point_generator.py`: This file contains functions for generating and exploring mapping points. It defines the following key functions:
- `blocking_partitioning_generator_function`: Generates blocking and partitioning configurations.
- `opt_get_best_loop_order`: Finds the best loop order for a given mapping point.
- `opt_mapping_point_generator_function`: Generates the best mapping point for a given resource and layer.
- `dataflow_exploration`: Explores different dataflows by iterating through various unrolled loop configurations and finding the one with the lowest energy cost.
3. `cost_model.py`: Contains functions to calculate the energy cost of various mapping points, validate mapping points, and get the cost of different memory levels.
4. `utils.py`: Provides utility functions for printing loop nests, calculating the product of a list, and other common operations.
5. `resource.py`: Defines the `Resource` class, which represents the hardware accelerator's resources, such as buffer sizes, parallelism levels, and MAC capacity.
6. `layer.py`: Defines the `Layer` class, which represents a CNN layer, including its dimensions (e.g., input, output, and filter sizes) and strides.
7. `loop_enum.py`: Contains enumerations for the loop types, such as input, weight, output, and their corresponding indices.
8. `mapping_point.py`: Defines the `MappingPoint` class, which represents a mapping point consisting of loop orders, loop blocking, loop partitioning, and parallelism dimensions.
Overview of the code of Interstellar-CNN-scheduler

## Slide 19
In the Interstellar-CNN-scheduler, loop blocking and resource allocation is achieved through the following steps:
Define hardware resources: The first step is to define the hardware resources available in the accelerator, such as processing elements, memory hierarchy levels, and parallelism capabilities. This information is encapsulated in the Resource class.
Generate possible blocking configurations: The `blocking_partitioning_generator_function` in the code generates possible blocking configurations for the given resource and layer. Each configuration represents different loop tiling/blocking sizes for the input, weight, and output tensors.
Validate blocking configurations: The code checks if a given blocking configuration is valid or not by ensuring that it doesn't exceed buffer size constraints at any level of the memory hierarchy. This is done using the `valid_mapping_point` function from the `cost_model` module.
Iterate through loop orders: For each valid blocking configuration, the tool generates possible loop orders using the `level_order_generator_function`. Loop orders determine the order in which nested loops are executed.
Evaluate the cost of each loop order: The energy cost of each loop order for a given blocking configuration is calculated using the `get_level_cost` and `get_array_and_curr_level_cost` functions from the `cost_model` module.
Find the optimal loop order: The best loop order is the one that has the lowest energy cost. The `opt_get_best_loop_order` function iterates through all the possible loop orders and selects the one with the lowest energy cost.
Generate mapping points: The best loop order, along with the blocking and partitioning configurations, is combined to form a mapping point. The `opt_mapping_point_generator_function` returns the best mapping point with the lowest energy cost for a given resource and layer.
Evaluate resource utilization: The scheduler calculates the resource utilization for each mapping point. This is done in the get_utilization function, which computes the ratio of utilized parallelism resources to the total available resources.
Through these steps, Interstellar-CNN-scheduler effectively applies loop blocking to optimize the hardware mapping of CNN layers. By minimizing the energy cost and maximizing resource utilization, loop blocking improves the overall performance of the hardware accelerator.
Loop Blocking and Resource Allocation

## Slide 20
In the Interstellar-CNN-scheduler, spatial loop unrolling is achieved through the following steps:
Generate partitioning configurations: The blocking_partitioning_generator_function generates different partitioning configurations for a given resource and layer. Each configuration represents the degree of parallelism applied to different loop levels. These parallelism levels are essentially spatial loop unrollings.
Create unrolled loop strings: For each partitioning configuration, the partitioned_loop_string function creates a string representation of unrolled loops. This string representation is used as a key in the dataflow exploration table.
Calculate utilization: The scheduler calculates the resource utilization for each partitioning configuration using the get_utilization function. This function computes the ratio of utilized parallelism resources to the total available resources.
Filter out low-utilization configurations (optional): If the accelerator supports replication and has a utilization threshold, the scheduler filters out mapping points with utilization lower than the threshold. This is done in the dataflow_exploration function.
Evaluate energy cost: For each valid partitioning configuration, the scheduler finds the optimal loop order that minimizes the energy cost using the opt_get_best_loop_order function. This function iterates through all possible loop orders and selects the one with the lowest energy cost.
Dataflow exploration: The dataflow_exploration function generates a table, with unrolled loop strings as keys and the best energy cost, utilization, and mapping point as values. By iterating through all the partitioning configurations and finding the best loop order for each, the scheduler can identify the optimal dataflow.
Select the best dataflow: After exploring all possible unrolled loop configurations, the scheduler selects the one with the lowest energy cost and, if applicable, above the utilization threshold. This configuration represents the optimal dataflow for the given CNN layer and hardware accelerator.
Through these steps, Interstellar-CNN-scheduler effectively applies loop blocking to optimize the hardware mapping of CNN layers. By minimizing the energy cost and maximizing resource utilization, loop blocking improves the overall performance of the hardware accelerator.
Spatial Loop Unrolling

## Slide 21
Thank you