## Slide 1: PROGRESS REPORT
Presented by: Suhas Somashekar
07/21/2023

## Slide 2: Tasks completed

## Slide 3: Preprocessing Improvement Overview
Additional functionalities introduced in the preprocessing stage.
Enhanced capabilities to analyze and track the computational graph's structure.
Operation Identification & Cataloguing:
  Identified 'Concat' and 'Add' operations between nodes.
  Catalogued for better comprehension and further usage.
  Helps in optimization, debugging, or enhancing the understanding of the underlying computational process.
Key Functionalities Implemented
Notes: Today, I would like to walk you through some enhancements we've made in the preprocessing stage of our compiler. We have introduced additional functionalities that boost our ability to analyze and track the structure of the computational graph.
Our focus has been twofold:
Firstly, we've placed significant emphasis on identifying and cataloging operations occurring between nodes in the computational graph. Specifically, we've looked at 'Concat' and 'Add' operations. Why is this important, you may ask? By cataloging these operations, we're able to gain a much clearer understanding of the dynamics at play across various nodes. This information is vital for future uses such as optimization, debugging, or for simply enhancing our understanding of the underlying computational process.

## Slide 4: Preprocessing Improvement Overview
Additional functionalities introduced in the preprocessing stage.
Enhanced capabilities to analyze and track the computational graph's structure.
Layer parameters extraction
Functionalities & Their Benefits
Layer Analysis:
  Isolated layer number and parameter type from model checkpoint state dictionary.
  Reordered layers based on their appearance, aiding in consistent layer indexing.
Parameter Calculation & Storage:
  Computed original (pre-normalization) weights and biases from batch normalization parameters.
  Stored processed parameters in a dictionary for further use, such as model tuning, analysis, or debugging.
Key Functionalities Implemented
Notes: In our second area of focus, we've tailored our function to cater specifically to streaming models and Ultranet. This has opened up new avenues for improved performance and functionality.
So, how did we do it? We begin with analyzing the layers of the model. We have a system that isolates the layer number and parameter type from the state dictionary of the model checkpoint. From here, we reorder the layers based on their sequence of appearance in the state dictionary, a simple yet effective strategy to ensure consistent layer indexing in subsequent operations.
Now, the crux of our enhancement is in the computation and storage of parameters. After traversing through the layer stats, our function computes the original weights and biases for each layer. This means that we process the batch normalization parameters to return the original, or pre-normalization, weights and biases of each layer. These are then stored in a dictionary for future use.
This process of deriving weights and biases from batch normalization parameters, which include gamma, beta, mean, and variance, allows us to efficiently use these parameters in the future for model tuning, analysis, or debugging.
In conclusion, the preprocessing enhancements we have implemented have led to more effective analysis of the computational graph, aiding our debugging and optimization efforts. We continue to push the boundaries of our capabilities, and we are excited to see where these improvements will take us next.

## Slide 5: Preprocessing Improvement Overview
Additional functionalities introduced in the preprocessing stage.
Enhanced capabilities to analyze and track the computational graph's structure.
Layer parameters extraction
Functionalities & Their Benefits
Layer Analysis:
  Isolated layer number and parameter type from model checkpoint state dictionary.
  Reordered layers based on their appearance, aiding in consistent layer indexing.
Parameter Calculation & Storage:
  Computed original (pre-normalization) weights and biases from batch normalization parameters.
  Stored processed parameters in a dictionary for further use, such as model tuning, analysis, or debugging.
Conclusion
The enhancements in preprocessing have resulted in improved analysis of the computational graph, aiding in debugging and optimization efforts.
Key Functionalities Implemented
Notes: Conclusion

## Slide 6: Streaming Compile -Performance and Memory Analysis
PE and SIMD Allocation
Aim: Optimal distribution of computational resources (SIMD units, PEs, DSPs) to each network layer considering FPGA hardware constraints.
Three allocation strategies introduced: 'PE', 'SIMD', 'Balance'.
The choice depends on the network architecture and FPGA hardware specifications.
Ensure total allocation does not exceed available DSPs on FPGA.
Result: Enhanced network efficiency and performance on FPGA.
RAM Usage Calculation
Purpose: Understand memory usage of a design on FPGA.
Reporting Block RAM (BRAM) and Ultra RAM (URAM) for each network layer when mapped onto FPGA.
Factors considered: Input Feature Map (IFM), operations being performed, and dimensions of input and output feature maps.
FPS Calculation
Purpose: Understand performance of the given FPGA configuration.
Aim: Calculate frame per second (FPS) rate for current FPGA configuration.
Process: Iterate over SIMD units, Processing Elements (PE), and Multiply-And-Accumulate operations (mul_opt) in each network layer.
Derive FPS: Calculate operations per clock cycle for each layer, compute total clock cycles required, and then derive FPS.
Notes: we will be delving into some of the recent improvements we've made in our streaming compiler. We've been focusing on three major areas: PE and SIMD allocation, Frames Per Second (FPS) calculation, and RAM usage calculation. Each of these improvements has been geared towards enhancing the efficiency and performance of our network deployment on FPGA.
Let's begin with our PE and SIMD allocation. The primary objective here has been to find the most effective distribution of our computational resources, specifically SIMD units, PEs, and DSPs, to each layer of the network. In order to give users the freedom to optimize based on their specific needs and constraints, we've introduced three allocation strategies. These include 'PE', 'SIMD', and 'Balance'. Now, it's important to note that the optimal mode may vary depending on both the network architecture and the specific specifications of the FPGA hardware. Of course, in all this, we always have to ensure that our total allocation does not exceed the DSPs available on the FPGA.
Moving on to the second major area of focus, FPS calculation. The aim here is to compute the frame-per-second rate that the FPGA can achieve under its current configuration. To do this, we iterate over the SIMD units, Processing Elements, and Multiply-And-Accumulate operations in each layer of a neural network. By calculating the number of operations that can be completed in a single clock cycle for each layer, we can derive the total number of clock cycles required for all operations in a given layer. This, in turn, allows us to compute the frames per second for each layer. The result? A comprehensive understanding of the performance of any given FPGA configuration.
Lastly, let's discuss RAM usage calculation. Here, our goal is to accurately calculate and report the required Block RAM, or BRAM, and Ultra RAM, or URAM, for each layer of a network when it's mapped onto an FPGA. These calculations are based on a variety of layer-specific factors, including its input feature map, the specific operations being performed, and the dimensions of the input and output feature maps. The end product of this calculation is a report on the total BRAM and URAM requirements, providing us with essential information for understanding the memory usage of a design on FPGA. I have also dedicated considerable effort to the Ultranet model, specifically with integrating it with our compiler. This required an in-depth understanding of the source code, and I took on the responsibility of connecting the dots between our existing code and the source code. Additionally, I tackled a variety of miscellaneous tasks including, but not limited to, developing a function to generate the C++ top_file code and modifying the quantization types.

## Slide 7: Next Steps

## Slide 8: Next Steps – Operation Fusion
What is Operation Fusion?
Optimization technique in deep learning compilers.
Combines multiple operations into a single one.
Primary goals: Reduce computational complexity and improve execution efficiency.
Why is Operation Fusion Important?
Reduces Kernel Launch Overhead: Minimizes operation launch overhead on GPU.
Improves Memory Access Efficiency: Optimizes data locality and reduces data movement.
Maximizes Hardware Utilization: Allows larger operations for better use of resources.
Reduces Memory Footprint: Minimizes need for intermediate storage, leading to less memory usage.
How we plan to achieve Operation Fusion?
Identify opportunities where multiple operations can be merged into a single one, taking into account factors like data dependencies, computational cost, and hardware capabilities.
Creates new, fused operations that replace original separate operations.
Develop a comprehensive support for all possible
Notes: Operation fusion is a vital optimization technique in deep learning compilers, especially for computational graphs in machine learning models. Its primary purpose is to reduce the computational complexity and improve the overall execution efficiency of the model. The idea behind operation fusion is to combine multiple operations into a single one, which results in reduced data movement, lower memory footprint, and increased parallelism. Why Operation Fusion is Important ? Reduces Kernel Launch Overhead: Every operation launch on GPU has a certain overhead. By fusing multiple operations together, we can minimize this overhead. Improves Memory Access Efficiency: Operation fusion often improves data locality and reduces the amount of data movement. The fused operation can use the data loaded into the fast on-chip cache memory of the GPU, leading to a much higher bandwidth than separate operations. Maximizes Hardware Utilization: Modern hardware accelerators like GPUs perform best when they can exploit high degrees of parallelism. Operation fusion allows for larger, more complex operations that better utilize these resources. Reduces Memory Footprint: By fusing operations, the need for intermediate storage (to hold the results of each operation) can be reduced, leading to less overall memory usage. How Operation Fusion is Achieved To achieve operation fusion, deep learning compilers use a graph-based representation of the model. Each node in this graph represents an operation (like convolution, batch normalization, etc.), and the edges represent the flow of data between operations. The deep learning compiler analyzes this graph and identifies opportunities where multiple operations can be merged into a single one, taking into account factors like data dependencies, computational cost, and hardware capabilities. Some of these transformations are straightforward (like merging convolution and batch normalization), while others might involve more complex restructuring of the computation graph. Once the opportunities for fusion are identified, the compiler generates new, fused operations that replace the original separate operations in the computation graph. This new graph is then used for generating the final, optimized code that executes on the hardware. Overall, operation fusion is an important aspect of optimizing deep learning models, helping to make these models more efficient and performant on modern hardware accelerators.

## Slide 9: Next Steps – High Throughput Quantized Convolution
Goal:
  Formulate a comprehensive function integrating vital parameters to enhance packing strategy and subsequently, improve throughput of CNNs' convolution operations.
Approach:
  Leverage parallel processing of multiple low-bit width convolution operations for increased computational throughput.
  Determine optimal guard bit length and cascade factor for efficient packing in any given hardware setup and input data.
Significance:
  Vital for different bit-width configurations.
  Aim to minimize computational overhead and maximize effective computational throughput.
Implementation Steps:
  Implementation of Mixed Integer Programming for optimal parameter identification.
  Parameters include length of guard bits, cascade factor for different hardware configurations.
Notes: Our goal is to formulate a comprehensive function that integrates essential parameters to enhance our packing strategy. "Packing" in this context refers to the efficient organization of input data and filters, also known as weights or kernels, for streamlined computations. An efficient packing strategy, therefore, has a direct impact on the throughput of CNNs' convolution operations.
Our approach focuses on capitalizing the capability of parallel processing of multiple low-bit width convolution operations. This results in significantly higher computational throughput.
The significance becomes evident when we consider different bit-width configurations. Each hardware setup may have its unique configuration, and our approach aims to cater to this diversity. We focus on minimizing the computational overhead while maximizing the effective computational throughput.
Regarding our implementation steps, we plan to employ Mixed Integer Programming. This mathematical approach of solving multiple constraints helps us to identify optimal parameters like the guard bit length and the cascade factor and they can be tailored to different hardware configurations.
In essence, we are attempting to implement a theoretically guaranteed technique to achieve significantly higher computation throughput while maintaining flexible bit widths.

## Slide 10
Thank You